# CGO3+ UART tool (CGO3PUARTtool)

## Abstract
This tool provides UART (serial) connection to the CGO3+ or CGO-ET for Typhoon H (not those for H520) camera.

Once connected the tool offers three functions:
- Act as gimbal checker. With this function you can read and record a lot of data coming from gimbal or camera itself. And you can try to calibrate the gimbal.
- Act as flight controller to tilt and rotate the camera. This offers the possibility to reuse the camera for other purposes. This part is only a demo.

The gimbal checker provides a possibility to fully calibrate the gimbal of the CGO3+. This functionality is experimental. Use it on your own risk.

Download this tool at download page: http://h-elsner.mooo.com/html/downl.htm
Binaries for Windows (.zip) and LINUX (.tar.gz) are available.

Installation: No installation, simply unzip the file. It is a portable application. You need only the executable for your OS. Copy it somewhere in the home file system or to an USB stick.

## CGO3+ gimbal calibration
NOTE: This is an experimental process, not an official tool. This may work or not, no warranty. You use it on your own risk.

### Preparation
You need a mount for the CGO3+ where it can rotate and tilt freely. Connect a Serial-USB converter (also known as programmer cable) to Gound, Rx and Tx. You can use The USB cable YUNA100 from Q500 if you have one or any other converter that has 3.3V level. Do not connect power. Rx and Tx must have 3.3V level.

This is a camera mount YUNTYH108. You need one with contact PCB.
Connect Ground to GND converter Tx to mTx/PWM and converter Rx to mRx.

My setup is a wooden mount for the camera and a serial to USB converter with a CP2104 chip.

This training video from Yuneec describes the calibration process:
https://www.youtube.com/watch?v=sATbbMajMCk

Please watch it before you try your first calibration.

### Process in short
- Power on the camera.
- Connect Serial to USB converter to CGO3+ UART.
- Start this application.

- Select the proper serial port.
 For Windows OS this is usually the last one in the list. It will be selected by default. If the COM
 port is missing double click on the port selection to refresh the list.
  For LINUX select ‘/dev/ttyUSB0’.
- Baud rate for those cameras is 115200 as default.
- Click on 'Connect‘
- Erase:
- Yaw encoder
- Zero phase
- Acc
- Front
- Begin with Yaw encoder calibration, wait until success message will appear.
- Hold the camera faced forward and leveled (I use the CGO3+ gimbal lock)
 and start Pre-front calibration.
- Then Zero phase calibration.
- Click on 'Disconnect'.
- Power cycle the camera.
- Click on 'Connect‘ again.
- Do Accelerometer calibration.
- Power cycle the camera.

Note: If „No ACC Offset„ will be reported or Accelerometer calibration never ends, then try a Camera Calibration on the drone started by ST16. If successful it will result in „ACC Offset OK“.

Simply buttons from up to down, always wait on success message.
## YTHtool as Flight controller (demo)

This is a demo project how to control tilt and pan by your own application. It offers all possibilities that ST16 has including Gimbal Calibration as it would be initiated from ST16 menu.

You can record the messages that come from camera (SysID=3) and gimbal (SysID=2). Data from MessageID=3 (Gimbal position) will be displayed in the 3 charts.

More information about communication between flight controller and gimbal/camera in "Format_CamUART_messages.ods".
See also the tool, described here: https://github.com/h-elsner/H480_UART_reading

## Troubleshooting
### UART connection problems
- If you start the app before you you connect the camera double click on the port selection field to update port list.
  For Windows usually the last (highest) COM port number is the one you need. It will be selected automatically.
  For LINUX the port /dev/ttyUSB0 is for the gimbal. If more then ACM ports are in use again the highest port number is probably the one you need.
- For other connection problems unplug und plug again of the USB cable may help.
- Also a reboot of the connected device may help. Do reboot always when USB is disconnected.
- Disconnect the UART in the app if you power off drone or the camera. It takes 2s before the app recognizes that the connection was cut.

### Gimbal calibration
If „No ACC Offset„ will be reported or Accelerometer calibration never ends, then try a Camera Calibration on the drone started by ST16.